Glossary for the Module

M06 - Choice of Participatory Mapping Method based on Purpose, Environment and Resources

Compiled by: Jon Corbett and Kasondra White

| Term | Definition | Source (if known) |
| --- | --- | --- |
| Aerial images | Aerial images are remote-sensed photographs taken from an airplane or some other aerial platform. | Wikipedia. http://tinyurl.com/2d2hgq |
| Geographic information systems (GIS) | GIS refers to computer-based systems designed to collect, store, manage and analyse spatially referenced information and associated attribute data. |  |
| Global positioning system (GPS) mapping | A GPS is a system of artificial satellites and ground units that enables a user with a portable receiver to accurately determine absolute locations using a standard coordinate system. | Flavelle, Alix. 2002. Mapping Our Land. Lone Pine Foundation, Edmonton, Canada. |
| Mylar sheets | These are sheets made of biaxially-oriented polyethylene terephthalate (boPET) polyester film, used for its high tensile strength, chemical and dimensional stability and transparency. Used as a clear overlay map for tracing additional data on a base map. | Adapted from http://www.wikipedia.org |
| Remote sensing | The process of gathering information about the Earth from a distance. ‘Remote’ because observation is done at a distance without physical contact with the object of interest. Such data is commonly gathered by satellite or aerial photography or other instrument-based techniques. | Digimap Guernsey http://tinyurl.com/3xn2e8e |
| Scale mapping | Scale mapping is a more sophisticated method of sketch mapping, aimed at generating geo-referenced data to facilitate discussions and allow community members to develop maps that contain true geographic scale that can stand the scrutiny of adversarial parties. The method is based on effective selection of symbols and colours for depicting community spatial knowledge on transparencies superimposed on a geo-coded and scaled map. | Mapping for Change, Participatory Learning and Action, PLA, Vol. 54. IIED 2006 |
| Surveying | Surveying means to traverse a particular linear feature (such as a boundary or a river), or travel in some specific pattern across a particular area, with the purpose of recording the locations of features on the land and details about them for use in making a map. A compass survey is done with a compass and metre tape; a GPS survey is done with a GPS receiver. | Flavelle, Alix. 2002. Mapping Our Land. Lone Pine Foundation, Edmonton, Canada |