Unit M09U04 - Compass Survey

Unit Trainer Notes

Outlined and developed by: Alix Flavelle

| Introduction | This Unit is all about working with a map and a compass. It covers the basics of how to use a compass, how to use a compass with a base map and how to design and conduct a compass traverse. A compass traverse may be used to map a small area accurately or to conduct an open-ended traverse. A traverse is often used in mapping for resource inventories. A compass traverse is time-consuming, so it is a method used for making scale maps of relatively small areas. It is a relatively simple step-by-step process to measure bearings and distances on the ground and then draw them to scale. This process therefore offers a hands-on way to clearly see and work with the basic elements of scale maps – the relationship between scale, distance and direction. |
| --- | --- |
| Target audience | Technology intermediaries working in multidisciplinary teams and operating within an institution/organisation already committed to practising participatory mapping and who are or would be required to: (i) deliver training on the practice; (ii) facilitate the process in the field. |
| Unit objectives / expected outcomes | After the completion of the Unit the trainee will be able to: describe the principles of a compass; use a compass with a map; use a compass in a survey or traverse of different patterns by measuring direction, distance, slope, etc.; conduct a compass traverse; plot and draw a traverse to make a basic map; give an overview of compass survey tools. |
| Keywords / key concepts | Bearing, compass traverse, station, point of commencement, slope distance, horizontal distance |
| Content outline, main topics covered and suggested sequencing | This Unit focuses on the topics listed below. How to work with a compass and a map (PPT No. 1: Using a Compass) (20 min) Using a compass to take bearings (Exercise No. 1: Using a Compass) (40 min) Using a compass with a map (Exercise No. 2: Finding Bearings on a Map) (60 min) Conducting a compass traverse (PPT No. 2: Compass Survey) (20 min) Estimating distance by pacing (Exercise No. 3: Pacing Distance) (40 min) (optional) Measuring slope angle and converting slope distance to horizontal distance (Exercise No. 4: Measuring Slope and Making Slope Conversions)(60 min) Build your own clinometer (Exercise No. 5: Make Your Own Clinometer)(60 min) (optional) Compass traverse (Exercise No. 6: Compass Traverse) (60 min) Processing compass survey data (PPT No. 2: Compass Survey, Part 2) (20 min) Plotting the compass traverse (Exercise No. 7: Plotting the Compass Traverse) (60 min) |
| Components of the Unit | Exercises Exercise No. 1: Using a Compass; to use a compass to find a bearing in the field (40 min) Exercise No. 2: Finding Bearings on a Map; to plot a bearing on a map, to extract a bearing from a map, to determine a location on a map using triangulation (60 min) Exercise No. 3: Pacing Distance; to perform a quick method for estimating distances on the ground (i.e. pacing) and to relate the sense of a distance and number of metres walked (40 min) (optional) Exercise No.4: Measuring Slope and Making Slope Conversions; to explain why slope distance and horizontal distance differs, to measure slope and calculate horizontal distance from a given slope distance and slope angle (60 min) Exercise No. 5: Make Your Own Clinometer; to visualise slope angles by using a visual tool to measure slope and to make a clinometer from inexpensive and easily available materials (60 min) (optional) Exercise No. 6: Compass Traverse; to apply knowledge of distance and bearing measurements to make a compass traverse and to coordinate a team effort to complete a compass traverse (60 min) Exercise No. 7: Plotting the Compass Traverse; to plot compass traverse data and calculate error of closure (60 min) Handouts for Trainee (to be distributed in printed format) Compass Survey (Handout4T) List of Additional Resources Glossary Multimedia None Presentations (PPT) PPT No.1: Using Compass and Map; shows trainees how to use a compass and map (30 min) PPT No. 2: Compass Survey; conducting a compass traverse and processing compass survey data (40 min) Unit Glossary Included in the Module Glossary |
| Duration | Working with compass and map – 2 hours Compass survey – 3 ½ – 5 hours Total for both methods – 7 hours |
| Prerequisite skills / knowledge | None |
| Pre-Unit activities | M09U01 M09U02 |
| Additional trainer resources | Hawkins, Peter. 2003. Map and Compass: The art of navigation. Milnthorpe: Cicerone Hodgson, Michael. 2000. Compass and Map Navigator: The complete guide to staying found. Conneticut, USA. Globe Pequot Press. Jacobson, Cliff 1997. Basic Essentials of Map and Compass. Merrillville, Indiana, USA. ICS Books. Pugh, John 1975. Surveying for field scientists. USA. Taylor & Francis. Finding Your Way with Map and Compass. Fact Sheet Source: US Geographic Service http://tinyurl.com/lt2jjv Last accessed: May 22, 2009 Description: An instructional overview of working with map and compass. Reading Topographic Maps Source: mapreading.com http://tinyurl.com/ngbj3h Last accessed: May 22, 2009 Description: Free online manual on reading topographic maps. Activities: Map and Compass Source: Iowa Department of Natural Resources. http://tinyurl.com/kvh42f Last accessed: May 22, 2009 Description: A series of activities for learning about map and compass; contour lines, and using compass with a map. |
| Equipment needed | Computer and beamer, compass (one compass for each four trainees if possible), topographic map or geo-referenced base map (if available), distance measuring tool (i.e. survey chain or laser finder), field note books (one per trainee), field pencil, eraser and colour pencils for each trainee, table surface, scientific calculator or cosine table, slope measuring device, graph paper, protractor, straight edge ruler, marker pen, cardboard, scissors or knife, string and weight (number depending on number of groups of trainees) |
| Comments | Adapt this Unit to your needs. Some mapping projects may involve just the section on Map and Compass, while others may also involve the section on Compass Survey. There are two PowerPoint (PPT) presentations. The first one – about using a map and compass – can be followed immediately by the related exercises. The other PPT – about how to conduct a compass survey – may be presented in two parts with exercises conducted immediately after each part. Although a compass traverse may not be needed for the purposes of the mapping project, working with a compass is a graphic and hands-on way of learning about scale maps. A compass survey is best learned by doing it. The PowerPoint presentation is intended to be brief and allow more time for the exercises and basic practice of conducting a compass traverse. Nevertheless do not rush through the PPT presentation; allow discussion and questions. |