Exercise No. 4: Measuring Slope and Making Slope Conversions

Developed by: Alix Flavelle

Objective:

To explain why slope distance and horizontal distance differ, to measure slope and to calculate horizontal distance from a given slope distance and slope angle

Time:

60 minutes

Materials:

Metre tapes, paper, pencils, scientific calculator or cosine table, slope measuring device

Procedure:

- Divide the group into as many small groups as possible with each group having a metre tape.

- Ask the members of each small group to measure the difference between slope distance and horizontal distance in the following way: One member of the group stands on a chair with the end of the metre tape. Another member stands about 4-5 metres away, pulls the metre tape tight and measures the distance. Then the person gets off the chair, stands right beside it and the other measures the distance again. Note the difference in distance. Make sure that everyone is holding the metre tape at the same height on their bodies for every measurement.

- Find a place where members in each group can stand about 20 metres apart on a slope. If there is no sloping ground, have one person stand on a balcony or on some stairs while the other person stands on the ground.

- Have the group member’s measure and record the slope distance with a metre tape. Then, measure and record the slope angle with whatever device is available. It may be a sighting clinometer, a compass with slope needle, a protractor and straight-edge or a handmade clinometer.

- Have the groups take their measurements and calculate the horizontal distance using the following equation:

Horizontal distance = slope distance x cosine of slope angle

- Photocopy the equation and cosine tables below for each small group.

Tips and options:

- Draw a diagram of slope distance as shown below and write the above equation on a flip chart for trainees to see.

- If available, use a variety of different slope measuring devices such as the needle on a compass, a clinometer or a hand-held protractor. Discuss which ones are easier to use and which are more accurate and why.

- Note that using the protractor is a visually clear way of seeing the slope angle.

- Write several imaginary measurements of slope distance and slope angle (e.g. 40 metres with a slope of 24o) on a blackboard or flipchart and have trainees calculate the horizontal distance.

Equation for slope conversion

Horizontal distance = slope distance x cosine of slope

Cosine Tables

- Cosine for slope angle in degrees

| Slope degrees | Cosine | Slope degrees | Cosine | Slope degrees | Cosine |
| --- | --- | --- | --- | --- | --- |
| 10 | 0.9849 | 22 | 0.9272 | 34 | 0.8290 |
| 11 | 0.9816 | 23 | 0.9205 | 35 | 0.8192 |
| 12 | 0.9781 | 24 | 0.9135 | 36 | 0.8090 |
| 13 | 0.9744 | 25 | 0.9063 | 37 | 0.7986 |
| 14 | 0.9703 | 26 | 0.8988 | 38 | 0.7880 |
| 15 | 0.9659 | 27 | 0.8910 | 39 | 0.7771 |
| 16 | 0.9613 | 28 | 0.8829 | 40 | 0.7660 |
| 17 | 0.9563 | 29 | 0.8746 | 41 | 0.7547 |
| 18 | 0.9511 | 30 | 0.8660 | 42 | 0.7431 |
| 19 | 0.9455 | 31 | 0.8572 | 43 | 0.7314 |
| 20 | 0.9397 | 32 | 0.8480 | 44 | 0.7193 |
| 21 | 0.9336 | 33 | 0.8387 | 45 | 0.7071 |

- Cosine for slope angle in percent

| Slope percent | Cosine | Slope percent | Cosine | Slope percent | Cosine |
| --- | --- | --- | --- | --- | --- |
| 10 | 0.9950 | 46 | 0.9085 | 74 | 0.8038 |
| 15 | 0.9889 | 48 | 0.9015 | 76 | 0.7962 |
| 20 | 0.9805 | 50 | 0.8944 | 78 | 0.7885 |
| 22 | 0.9766 | 52 | 0.8872 | 80 | 0.7809 |
| 24 | 0.9724 | 54 | 0.8799 | 82 | 0.7733 |
| 26 | 0.9678 | 56 | 0.8725 | 84 | 0.7657 |
| 28 | 0.9630 | 58 | 0.8650 | 86 | 0.7582 |
| 30 | 0.9578 | 60 | 0.8575 | 88 | 0.7507 |
| 32 | 0.9524 | 62 | 0.8499 | 90 | 0.7433 |
| 34 | 0.9468 | 64 | 0.8423 | 92 | 0.7359 |
| 36 | 0.9409 | 66 | 0.8346 | 94 | 0.7286 |
| 38 | 0.9348 | 68 | 0.8269 | 96 | 0.7214 |
| 40 | 0.9285 | 70 | 0.8192 | 98 | 0.7142 |
| 42 | 0.9220 | 72 | 0.8115 | 100 | 0.7071 |
| 44 | 0.9153 |  |  |  |  |